## Slide 1: Cloud-Offloaded GPS
Jie Liu
Microsoft Research Redmond, WA 98052
Jie.liu@microsoft.com
Mobile Location Sensing Tutorial at MobiSys 2013

## Slide 2: GPS Receiving
Tracking
Acquisition
SV IDs
Decoding
Code Phases
Ephemeris
Least Square
Baseband
(lat, lon)
Time stamp
Code Phases
Doppler
Every ms continuous
Time stamp: 6s
Ephemeris: 30s
~10ms
TLM
HOW
Clock corrections and SV health
TLM
HOW
Ephemeris parameters
TLM
HOW
Almanac
TLM
HOW
Almanac, ionospheric model, dUTC
TLM
HOW
Ephemeris parameters
6
12
18
24
30
Time (sec)
300 bits (10 words)
preamble
Time of week
in the cloud!
1 ms data (4kB)
Intense computation

## Slide 3: Coarse Time Navigation
Time of flight has two parts
  Fractional part – code phase
  Integer part (# of ms, NMS)
Nearby locations have the same NMS.
A reference location and a coarse time remove the need for timestamp decoding.
code phase
NMS （~60ms)
time of flight (ms) = code phase + # of ms (NMS)
fraction
integer
NMS
~100km

## Slide 4: Course Time Error vs Common Bias
Common bias causes same error in all distance measurements

## Slide 5: Course Time Error vs Common Bias
Common bias causes same error in all distance measurements
Course time errors are different for each measurement.

## Slide 6: New Observation Equations
Solve by linearization near
Need 5+ satellites

## Slide 7: Solve Integer Roll Over Problem
When code phase is close to 0 and common bias is small
Solution:
  Choose one satellite as a reference and cancel out common bias
ms
Nms from ref loc
Code phase
Real prop time
satellite clock error
Common bias
Estimated prop time
Estimation error
noise

## Slide 8: Solve Integer Roll Over Problem
Subtract the two
Assume < 0.5ms
Round down

## Slide 9: Time Drift Evaluation
(s)

## Slide 10: Online Ephemeris
Broadcast Ephemeris (RINEX)
http://igscb.jpl.nasa.gov/components/dcnav/cddis_data_daily_yyn.html
National Geodetic Survey (NGS):http://www.ngs.noaa.gov/orbits/
  Ultra-rapid (iguWWWWD.sp3) 6-hour latency
  Rapid (igrWWWWD.sp3) 13-hour latency
  Final (igsWWWWD.sp3) 12 to 14 day latency

## Slide 11: SP3 Files
For full specification http://www.ngs.noaa.gov/orbits/SP3_format.html
* 2013 6 20 0 0 0.00000000
P 1 15833.341744 0.164576 21320.746257 39.638737
V 1 8522.699138 25731.050460 -6232.897765 0.046098
P 2 -13705.126878 -21928.324527 -6915.898362 437.855352
V 2 -401.124411 -9435.761633 29274.903151 0.017941
P 3 21932.968373 9793.907906 -12084.896943 222.312056
V 3 -14624.350974 2137.876854 -25721.177094 0.048538
position (km)
clock correction (ms)
velocity (km/s)
clock drift (10-4 ms/s)
GPS Time, every 15 minutes

## Slide 12: Without Reference Location?

## Slide 13: Disambiguating Reference Locations
Conjecture: Least square may not converge

## Slide 14: Disambiguating Reference Locations
Use Doppler shifts
Similar observation equations can be derived
Doppler uncertainty results in wider intersection region
Receiver Location at cone intersection(s) on the Earth’s surface

## Slide 15: Disambiguating Reference Locations
The 3rd dimension:
  Use elevation data from cloud services, e.g. USGS Elevation API: http://www.programmableweb.com/api/usgs-elevation-query-service
S1
S2
A
B
C
D
E
F
H
G
I

## Slide 16: Cloud-Offloaded GPS Design
Raw GPS signals (16MHz sampling rate, 2 bit/sample, 2ms)
“reasonable” time stamp
Acquisition
SV IDs
Code Phases
NASA/NGA Orbit DB
Ephemeris
Coarse Time Navigation
Device (a set of 2ms GPS signals)
Device Timestamp
(lat, lon, alt)
AOA Intersection
Ref. Locations
Doppler
SV speed
Time stamp
Cloud

## Slide 17: CLEON Prototype
Max 2769 GPS receiver
MSP430F5338 mC, 12MHz
Serial to parallel + DMA
Rechargeable battery
Battery-backed up real-time clock
microSD card

## Slide 18: Device Energy Performance: (flash chip)
action | Current(mA) | Duration (ms)
GPS sampling | 42 | 2.2
Flash writing | 1.5 | 28.8
Total (2ms) | 4.37 | 31
GPS sampling
Save to flash
5x 2ms GPS sample: ~2mJ
1 A-GPS sample in phone: ~2J
In theory, 2AA batteries (2Ah) can last for 1.5 years with continuous GPS sampling (1Hz).

## Slide 19: Low Energy Assisted Positioning Cloud Service
Azure Cloud
Web Role
Queue
LEAP Workers
SQL Azure
Ephemeris table
Eph. Worker
NGA/ NASA
Web Role
Client ID, data
Req. ID
Client ID, Req. ID
Location
https://msr-leap.cloudapp.net/LEAP.svc

## Slide 20: Web Services Demo

## Slide 21: Source of Errors
Visible Satellites
Multi-path effect
Ephemeris accuracy
Time stamping accuracy

## Slide 22: Accuracy Evaluation
~1500 set of traces, 10~60s long each (~50GB)
Taken from both northern and southern hemisphere (US, Brazil, Korea).
chunk
gap
…
sampling
idle
# of Chunks | Chunk Length (ms) | Gap Length (ms)
1 | {2, 4, 6, 8, 10} | 0
{1, 2, 3, 4, 5} | 2 | 50
5 | 2 | {0, 10, 50, 100}

## Slide 23: Number of Acquired SVs

## Slide 24: Accuracy Evaluation
2ms, 3~5chunks, 50ms gaps
16X oversampling (2ms == 8KB)
Min | Median | Mean | Max | StdDev
0.06 | 11.85 | 20 | 725.08 | 33.65
Chart: Error Distrubtion (CDF)
| 5 | 10 | 15 | 20 | 30 | 40 | 50 | More
 | 0.22 | 0.42 | 0.58 | 0.7 | 0.83 | 0.9 | 0.93 | 1

## Slide 25: Number of acquired satellites
Chart: Accuracy vs Acquired Satellites (5 chunks)
| 5 | 6 | 7 | 8 | 9 | 10
5m | 0.22 | 0.26 | 0.25 | 0.22 | 0.24 | 0.55
10m | 0.19 | 0.19 | 0.23 | 0.25 | 0.22 | 0.15
15m | 0.17 | 0.14 | 0.18 | 0.22 | 0.27 | 0.15
20m | 0.04 | 0.1 | 0.12 | 0.12 | 0.18 | 0
30m | 0.09 | 0.13 | 0.13 | 0.11 | 0.07 | 0.15
40m | 0.02 | 0.1 | 0.05 | 0.04 | 0 | 0
more | 0.27 | 0.08 | 0.04 | 0.04 | 0.02 | 0

## Slide 26: Other GPS Snapshot Platforms
U-Blox YUMA (Switzerland)
  200ms capture
PathTrack FastLoc (UK)
  150ms capture
Cell-Guide Robin (Israel)
  >64ms capture

## Slide 27
A Spectrum of GPS Solutions
 |  |  |  |  | Self-contained GPS
Example |  |  |  |  | Car GPS
Acquisition |  |  |  |  | On device
Time Stamp |  |  |  |  | From satellites
Ephemeris |  |  |  |  | From satellites
Location Calc. |  |  |  |  | On device
Network Usage |  |  |  |  | None
Accuracy |  |  |  |  | 10m
Latency |  |  |  |  | ~30sec
Device Energy Consumption |  |  |  |  | ~10J
* Assume: 50mW GPS power and 1s acquisition latency; 50mW AP low and 1W AP high utilizations.

## Slide 28
A Spectrum of GPS Solutions
 |  |  |  | Precise-Time AGPS | Self-contained GPS
Example |  |  |  | Phone GPS today | Car GPS
Acquisition |  |  |  | On device | On device
Time Stamp |  |  |  | From satellites | From satellites
Ephemeris |  |  |  | From server | From satellites
Location Calc. |  |  |  | On device | On device
Network Usage |  |  |  | Ephemeris updates (1/6hrs) | None
Accuracy |  |  |  | 10m | 10m
Latency |  |  |  | ~6sec | ~30sec
Device Energy Consumption |  |  |  | ~2J | ~10J
* Assume: 50mW GPS power and 1s acquisition latency; 50mW AP low and 1W AP high utilizations.

## Slide 29
A Spectrum of GPS Solutions
 | Full Cloud Offloaded GPS |  |  | Precise-Time AGPS | Self-contained GPS
Example | Sensors, wearable |  |  | Phone GPS today | Car GPS
Acquisition | In cloud |  |  | On device | On device
Time Stamp | From device |  |  | From satellites | From satellites
Ephemeris | In cloud |  |  | From server | From satellites
Location Calc. | In cloud |  |  | On device | On device
Network Usage | Bulk or None |  |  | Ephemeris updates (1/6hrs) | None
Accuracy | 30m |  |  | 10m | 10m
Latency | Offline |  |  | ~6sec | ~30sec
Device Energy Consumption | ~2mJ |  |  | ~2J | ~10J
* Assume: 50mW GPS power and 1s acquisition latency; 50mW AP low and 1W AP high utilizations.

## Slide 30
A Spectrum of GPS Solutions
 | Full Cloud Offloaded GPS | Half Cloud Offloaded GPS |  | Precise-Time AGPS | Self-contained GPS
Example | Sensors, wearable | Mobile (logging) |  | Phone GPS today | Car GPS
Acquisition | In cloud | On device |  | On device | On device
Time Stamp | From device | From device |  | From satellites | From satellites
Ephemeris | In cloud | In cloud |  | From server | From satellites
Location Calc. | In cloud | In cloud |  | On device | On device
Network Usage | Bulk or None | Bulk or real-time |  | Ephemeris updates (1/6hrs) | None
Accuracy | 30m | 30m |  | 10m | 10m
Latency | Offline | Offline or <1s* |  | ~6sec | ~30sec
Device Energy Consumption | ~2mJ | ~100mJ (logging)* 1~2J (real-time)^ |  | ~2J | ~10J
Assume 1s acquisition at 50mW

## Slide 31
A Spectrum of GPS Solutions
 | Full Cloud Offloaded GPS | Half Cloud Offloaded GPS | Coarse-Time AGPS | Precise-Time AGPS | Self-contained GPS
Example | Sensors, wearable | Mobile (logging) | Mobile (real-time) | Phone GPS today | Car GPS
Acquisition | In cloud | On device | On device | On device | On device
Time Stamp | From device | From device | From device | From satellites | From satellites
Ephemeris | In cloud | In cloud | From server | From server | From satellites
Location Calc. | In cloud | In cloud | On device | On device | On device
Network Usage | Bulk or None | Bulk or real-time | Ephemeris updates (1/6hrs) | Ephemeris updates (1/6hrs) | None
Accuracy | 30m | 30m | 30m | 10m | 10m
Latency | Offline | Offline or <1s* | <1.2s * | ~6sec | ~30sec
Device Energy Consumption | ~2mJ | <100mJ (logging)* 1~2J (real-time)^ | <250mJ* | ~2J | ~10J
15ms on Surface Pro
Assume 10x slow down on phones

## Slide 32
A Spectrum of GPS Solutions
 | Full Cloud Offloaded GPS | Half Cloud Offloaded GPS | Coarse-Time AGPS | Precise-Time AGPS | Self-contained GPS
Example | Sensors, wearable | Mobile (logging) | Mobile (real-time) | Phone GPS today | Car GPS
Acquisition | In cloud | On device | On device | On device | On device
Time Stamp | From device | From device | From device | From satellites | From satellites
Ephemeris | In cloud | In cloud | From server | From server | From satellites
Location Calc. | In cloud | In cloud | On device | On device | On device
Network Usage | Bulk or None | Bulk or real-time | Ephemeris updates (1/6hrs) | Ephemeris updates (1/6hrs) | None
Accuracy | 30m | 30m | 30m | 10m | 10m
Latency | Offline | Offline or <1s* | <1.2s* | ~6sec | ~30sec
Device Energy Consumption | ~2mJ | <100mJ (logging)* 1~2J (real-time)^ | <250mJ* | ~2J | ~10J

## Slide 33: CO-GPS Demo