## Slide 1: Predictable performance optimization for wireless networks
Ratul Mahajan
Microsoft Research
Joint work with Yi Li, Lili Qiu, Eric Rozner, Yin Zhang (UT, Austin)

## Slide 2: Wireless performance is unpredictable
Even basic questions are hard to answer
  How much traffic can a given network support?
  What happens if a new flow starts?
  What happens if a node is removed?
Arguably the most frustrating aspect of wireless
  Mysteriously inconsistent performance
  Makes it almost impossible to plan and manage

## Slide 3: An example of performance weirdness
Source
Relay
Sink
Good
Bad
Source
Relay
Sink
Bad
Good
UDP throughput (Kbps)
Loss rate on the bad link
good-bad
bad-good
Testbed
Loss rate on the bad link
UDP throughput (Kbps)
good-bad
bad-good
2x
Simulation
bad-good
good-bad
Source rate (Kbps)
UDP throughput (Kbps)

## Slide 4: Predictable performance optimization
Given a (multi-hop) wireless network:
Can its performance for a given traffic pattern be predicted?
Can it be systematically optimized per a desired objective such as fairness or throughput?
Yes, and Yes, at least in the context of WiFi

## Slide 5: Our approach: measurement-based modeling and optimization
Measure the RF profile of the network
Constraints on sending rate and loss rate of each link
Find compliant source rates that meet the objective

## Slide 6: Measurements
One or two nodes broadcast at a time
Yields information on loss and deferral probabilities
Measure the RF profile of the network
Constraints on sending rate and loss rate of each link
Find compliant source rates that meet the objective

## Slide 7: Modeling
Constraints on sending rate and loss rate of each link
Find compliant source rates that meet the objective
O(n2) constraints
Link throughput is a function of loss rate and tx probability
Link tx probability is a function of tx probability of other links and deferral probability
Link loss rate depends on tx probability of other links
Tx probability is bounded by a function of loss rate
Measure the RF profile of the network

## Slide 8: Optimization
Constraints on sending rate and loss rate of each link
Find compliant source rates that meet the objective
Inputs:
Traffic matrix
Routing matrix
Optimization objective
Output:
Per-flow source rate
Measure the RF profile of the network

## Slide 9: Accuracy of throughput prediction in a testbed
Chart: Actual / predicted throughput
| 0.62600611910000004 | 0.6348235294000002 | 0.70990502040000025 | 0.73647222220000019 | 0.74637491840000025 | 0.8813513514000002 | 0.88640429340000026 | 0.95281329920000002 | 0.96018589250000042 | 0.96096096099999972 | 0.96640830879999973 | 0.96907150480000004 | 0.97934551640000023 | 0.98847727760000004 | 0.98854465479999998 | 0.98887227680000001 | 0.9897046233000002 | 0.98985236019999978 | 0.99162172570000007 | 0.99336131669999994 | 0.99432867879999998 | 0.99433142860000001 | 0.99913213889999974 | 0.99941792779999961 | 0.99955535789999983 | 0.99961007130000001 | 0.99988901220000026 | 0.99997939840000005 | 1 | 1
No scaling | 0.033333 | 0.066667 | 0.1 | 0.13333 | 0.16667 | 0.2 | 0.23333 | 0.26667 | 0.3 | 0.33333 | 0.36667 | 0.4 | 0.43333 | 0.46667 | 0.5 | 0.53333 | 0.56667 | 0.6 | 0.63333 | 0.66667 | 0.7 | 0.73333 | 0.76667 | 0.8 | 0.83333 | 0.86667 | 0.9 | 0.93333 | 0.96667 | 1
Scale = 10% | 0.033333 | 0.066667 | 0.1 | 0.13333 | 0.16667 | 0.2 | 0.23333 | 0.26667 | 0.3 | 0.33333 | 0.36667 | 0.4 | 0.43333 | 0.46667 | 0.5 | 0.53333 | 0.56667 | 0.6 | 0.63333 | 0.66667 | 0.7 | 0.73333 | 0.76667 | 0.8 | 0.83333 | 0.86667 | 0.9 | 0.93333 | 0.96667 | 1
Scale = 50% | 0.033333 | 0.066667 | 0.1 | 0.13333 | 0.16667 | 0.2 | 0.23333 | 0.26667 | 0.3 | 0.33333 | 0.36667 | 0.4 | 0.43333 | 0.46667 | 0.5 | 0.53333 | 0.56667 | 0.6 | 0.63333 | 0.66667 | 0.7 | 0.73333 | 0.76667 | 0.8 | 0.83333 | 0.86667 | 0.9 | 0.93333 | 0.96667 | 1

## Slide 10: Benefit of throughput optimization in a testbed
Chart: Number of flows
| 1 | 2 | 4 | 8 | 12 | 16
Without optimization | 1.0561 | 2.6285 | 1.7178 | 0.7823 | 1.1566 | 1.5583
With optimization | 1.0465 | 2.6108 | 2.6901 | 4.1637 | 4.3632 | 5.1736

## Slide 11: Lessons learned
Simple measurements on off-the-shelf hardware can provide accurate and tractable RF profile [SIGCOMM2006]
  Compare with abstract models (e.g., distance) or direct, detailed measurements
It is possible to model interference, MAC, and traffic in a way that balances fidelity and tractability [MobiCom2007]
  The three are inter-dependent
Holistically controlling source rates is important for achieving desired outcomes [SIGCOMM2008]
  Impact of transmissions not limited to the traversed path

## Slide 12: More challenges ahead
Changing spectrum availability and no fixed transmission channels
Newfangled receivers
Heterogeneous MACs
Multiple competing networks
……
As we move towards a brave new wireless world, performance predictability should be a central goal