## Slide 1: The Case of Software Defined Radio with MSRA (work-in-progress)
Yongguang Zhang
with Kun Tan, Fan Yang, Jiansong Zhang, Haitao Wu, Chunyi Peng, Songwu Lu
Microsoft Research Asia
June 2008

## Slide 2: Fundamental Challenges of SDR
Digital baseband processing
  Super computation required
  E.g. traditional 802.11a requires > 50Gops
Tight real-time response
  E.g. generate MAC response within 10us
High level of programmability
  Accommodate a large range of heterogeneous PHY algorithms and MAC protocols
Notes: Intel Xeon provides 13Gops

## Slide 3: Impending Technology Sea Change
Emerging multi-core/many-core GPP
  Today’s nVidia GPU: 256 core, 600GFlops
  Intel 80-core CPU: TFlops, IBM Cell: 200GFlops
  Predicted to possess 1000 cores in a few years
Opportunities
  Sufficient computational power and parallelism
  PHY MAC NET … APP processing in one place
Question: is general-purpose PC architecture suitable for SDR?

## Slide 4: Our Project Goals
Explore new ways of building DSR based on standard multi-core PC architecture
Develop a complete software stack
  High-speed PHY processing on GPP
  Support for time-critical MAC control
Provide a software system research platform for wireless communication and networking
Notes: Should we customize this goal for the talk????

## Slide 5: System Architecture
GPP+MEM
PCIe Bus
LPA/Sampling Convertor/DAC/ADC
Latency critical radio control (AGC/PD)
Antenna
SDR mgnt
Flexible RF Hardware
Network layer and above
Link-layer Processing
MAC Processing
Baseband Processing
Multi-core
Software
Radio
Architecture

## Slide 6: Flexible Radio Control Hardware
FPGA board to connect RF and PC bus
  PCIe-8x, Descriptor-based DMA, 256MB onboard SDRAM cache
Basic functions
  Fast sample transport b/w RF and PC memory
  AGC
  Packet Detection
  Early interrupt trigger
  Timing control
Xilinx Vertex5
FPGA
PCI-e Link to PC
GPIO: connect to RF

## Slide 7: Baseband Processing with GPP
Exploit parallelisms in PHY for multi-core
  Batching for SIMD and inter-symbol parallelism
  Control batch size to meet latency requirement
Exploit large memory and high-speed L2 cache
  Pre-calculations and lookup tables
    Convolution encoding
    (de)scramble, (de)interleaving, (de)mapper, …
Two paths
  Multi-core CPU (intel quad-core)
  Many-core GPU (nvidia GeForce 8800)

## Slide 8: Performance Results (intermediate)
Hardware throughput
Baseband processing speed (over link speed)
 | Rx | Tx
PCIe-x4 | 842 Mbps | 839 Mbps
PCIe-x8 | 1684 Mbps | 1675 Mbps
 |  | Parameters | Speedup
1-core CPU | 802.11b TX | Long preamble, 11Mbps | 29.59x
 |  | Short preamble, 11Mbps | 28.82x
 | 802.11b RX | Long preamble, 11Mbps | 2.83x
 |  | Short preamble, 11Mbps | 2.67x
128-core GPU | 802.11a TX | 54Mbps | 1.39x
 | 802.11a RX (w/o viterbi) | 54Mbps | 1.56x
 | 802.11a RX (w/ viterbi) | 54Mbps | 0.53x

## Slide 9: Performance Results (cont'd)
Hardware latency
 | DMA Read | DMA Write | Interrupt
PCIe-x4 | 0.36µs | 0.72µs | 7~10µs
PCIe-x8 | 0.34µs | 0.68µs | 7~11µs
 | TX Path | RX Path
RCB | 0.75µs | 1.75µs
RxTxTurnaroundTime < 5µs
RxTxSwitchTime < 5µs
Interrupt
Rx Latency.
Tx Latency.
Packet Detected
AGC Settle down
PLCP
Channel estimation
Data demodulation & decoding
CRC check and MAC hdr check
SIFS.
ACK send
ACK Prep.
Preamble
PLCP
Header
Data
GPP
H/W
Notes: RxTxTurnaroundTime ::= The maximum time that the PHY requires to change from receiving to transmitting the start of the first symbol.
RxTxSwitchTime ::= The nominal time that the PMD takes to switch from Receive to Transmit.

## Slide 10: Research Opportunities
Operating system support for SDR
  Resource management for multi-core
  High-resolution timer, scheduler
Programmability
  Library, reusable components
  Development tools
New thinking in wireless communications under extra computational power

## Slide 11: MAC Core: Precise Timing Control
Kernel service for time-critical MAC processing
  On-demand dedicate core for MAC state-machine
    Polling for events when going into time-critical task
    Microsecond level timing control
  Two-phase transmission transaction
    Pre-catch frame symbols in RCB
Time synchronization
  H/W timestamp for transceiving events
  Library functions to manage time mappings
Notes:   Preparation phase – load frame symbols onto RC board
  Medium access phase – involve MAC state-machine to control channel access

## Slide 12: Modular Link Layer
Modular software architecture for none time-critical link layer functions
  Extensibility
  Code reuse
Abstract each component into an object with typed interfaces
  Decouple functionalities into small objects
  Objects are interconnected with interfaces

## Slide 13: Graph Presentation of Link Layer
Flexible definitions of interfaces
  Data passing interfaces vs. control interfaces
Versatile connection types
  One-to-one; one-to-many; many-to-one; many-to-many
Components – realized as C++ objects
XML description for configuration file
Classifier
HighQ
LowQ
Sched
ARQ
CA
IfDataPush
IfDataPull
IfPreempt
IfFlush

## Slide 14: GUI-based Graph Generator
<?xml version="1.0"?>
<DriverGraph xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance xmlns:xsd="http://www.w3.org/2001/XMLSchema">
<Components>
<Component>
<Name>CCapDe</Name>
<Interfaces> <string>IfDataPush</string> </Interfaces>
<Connectors> <string>IfDataPush</string> </Connectors>
<Properties />
</Component>
</Components>
...
<ComponentInstances>
<ComponentInstance>
<Name>cap0</Name>
<TypeName>CCapDe</TypeName>
<PropertyNames />
<PropertyValues />
</ComponentInstance>
<ComponentInstance>
<Name>q0</Name>
<TypeName>CQueue</TypeName>
...
</ComponentInstance>
</ComponentInstances>
…
<Connections>
<Connection>
<CompAName>cap0</CompAName>
<CompBName>q0</CompBName>
<connectorName>IfDataPush</connectorName>
<interfaceName>IfDataPush</interfaceName>
<connectorNum>0</connectorNum>
</Connection>
</Connections>
</DriverGraph>
Type definition
Objects definition
Links definition
Notes: Note1: Add a screen

## Slide 15: Summary and Status
A new software radio stack based on PC architecture that supports
  High-speed PHY processing
  Low latency and time-critical MAC
  Modular architecture for link layer functions
Current status
  PCIe-based flexible radio control board
  Prototype and evaluate GPU and CPU based BB modules
  Prototype for MAC-Core runtime and modular link layer
  Integrating the whole research platform
Notes: Note 1: Add

## Slide 16: Thanks and Questions!