## Slide 1: GPS Fundamentals
Jie Liu
Microsoft Research
Redmond, WA 98052
Jie.liu@microsoft.com
Mobile Location Sensing Tutorial at MobiSys 2013

## Slide 2: GPS Basics
32 Satellites (SVs)
Ground management stations
Time synced to nanosecond level
Estimate trajectories for each SV
Transmit time and trajectory parameters (Ephemeris) periodically
Receiver estimates its location by:
  time of flight (pseudorange) from each visible satellite
  SV locations at time when signals left SVs.

## Slide 3: GPS Data Packets @50bps
TLM
HOW
Clock corrections and SV health
TLM
HOW
Ephemeris parameters
TLM
HOW
Almanac
TLM
HOW
Almanac, ionospheric model, dUTC
TLM
HOW
Ephemeris parameters
6
12
18
24
30
Time (sec)
300 bits (10 words)
preamble
Time of week

## Slide 4: GPS Time
GPS Time is a uniformly counting time scale beginning at the 1/5/1980 to 1/6/1980 midnight. January 6, 1980 is a Sunday.
GPS Time counts in weeks and seconds of a week from this instant. The weeks begin at the Saturday/Sunday transition. This is week 1746.
The days of the week are numbered, with Sunday being 0, 1 Monday, etc.
There are no "leap seconds" in this time system. Currently, GPS is ahead of UTC by 15 SECONDS.

## Slide 5: Gps signal structure
Each GPS satellite transmits continuously using two radio frequencies in the L-band, where:
All codes initialized once per GPS week at midnight from Saturday to Sunday
  Chipping rate for C/A is 1.023 MHz
  Chipping rate for P(Y) is 10.23 MHz

## Slide 6: GPS Signals Modulation
Using CDMA, satellite k sends signal:
    Received signal:
1023 kbps repeats every 1ms
C/A: Coarse/Acquisition

## Slide 7: GPS Signals Modulation
Using CDMA, satellites send the signal:
    Received signal:
1.575GHz
50 bps
1023 kbps repeats every 1ms

## Slide 8: GPS Signals Modulation
Using CDMA, satellites send the signal:
    Received signal:
1.575GHz
50 bps
1023 kbps repeats every 1ms
DSSS

## Slide 9: GPS Signals Modulation
Using CDMA, satellites send the signal:
    Received signal:
1.575GHz
50 bps
1023 kbps repeats every 1ms
DSSS, 280~460W

## Slide 10: Received Signal
After travel 20,000 km the receiver power is watts
Natural noise and man-made radio-frequency interference are much stronger than the GPS signal.
The signal power must be amplified by approximately ten orders of magnitude.

## Slide 11: GPS Receiver
.
.
Antenna
Burnout protection
Bandpass filter
Low-noise amplifier
Amplifiers
Down converters
Bandpass filters
A/D
Satellite #1
Acquisition
Tracking
Data Dem.
Analog signals
Application-Specific processing
Estimation of:
Position
Velocity
Time
Digital signals

## Slide 12: GPS Receiver Signal Processing
Analog signals:
  Signal conditioner
  Removes interfering signals in adjacent frequency bands
  Amplifies the power of the signal by
  Reduces the carrier frequency of 1575.42 MHz by a factor between 10 and 1000 – intermediate frequency
A/D converter – bandpass sampling
  Sampling rate is dominated by the bandwidth of the signal (not the highest frequency component)
  Up to order of 100 MHz

## Slide 13: GPS Receiver Signal Processing
Digital signals:
  Doppler removal
  Correlators
  Delay lock loop filter
  Phase lock loop filter
  Data demodulation
  Application specific processing
Figure courtesy: F. Van Diggelen “A-GPS”

## Slide 14: Auto-Correlation
Correlation peaks, every millisecond.

## Slide 15: Doppler Shifts
A rising GPS satellite can move at up to 800m/s towards a receiver, causing a frequency shift of L1*800/c = 4.2kHz, where c is the speed of light.
Simulated acquisition with no noise.
Figure courtesy: F. Van Diggelen “A-GPS”

## Slide 16: Acquisition Result
Doppler bins (500Hz)
Code phases

## Slide 17: Tracking
Continuous local peak adjustment based on acquisition results
. . . . . .
.
.
.
Code phase
Doppler bins

## Slide 18: Pseudorange Estimation
code phase
NMS （~70ms)
TLM
HOW
Ephemeris
TLM
HOW
Ephemeris
TLM
HOW
Ephemeris
s1
s2
s3
t1
t2
t3
TLM
HOW
Ephemeris
s4
t4
T
Distance:
Receiving time
Time signal left satellite i

## Slide 19: Distance Estimation
Clocks have errors: ,
Distance:
Absolute time
Local drift: common bias
Satellite drift: sent in message
Real distance
Important to use satellite position at transmit time. Satellites can move up to 60m during propagation time.

## Slide 20: Find Transmission Time
Many possible methods.
Light time equation (assume a few ms, and a loc. estimate)
…

## Slide 21: Observation Equations
Solve by linearization near
Observation Equations:

## Slide 22: Dilution of Precision
Measure the error sensitivity. smaller is better.
  1meter std in measurement gives xDOP std in results.
HDOP
PDOP is considered good.

## Slide 23: A-GPS
Two types:
  Mobile Station Assisted AGPS
  Mobile Station Based AGPS
Cloud send assisted information to mobile devices
  Ephemeris (typically valid for 6 hours)
  Visible satellites at any given time
  Doppler for each satellite at any given time

## Slide 24: Android Low Level GPS Log
+++++++++++ starting ++++ 1362715901273
GPSSC:STARTED:1362715901296
1524:NMEA:1362715902:$GPGSA,A,1,,,,,,,,,,,,,,,*1E
…
10790:SATs:1,31.0,93.0,44.0:8,27.0,354.0,59.0:11,27.0,63.0,41.5:17,30.0,237.0,39.0
10826:NMEA:1362715912:$GPGSV,1,1,04,08,59,354,26,17,39,237,30,01,44,093,30,11,41,063,26*7A
…
15884:SATs:1,24.0,133.5,47.0:8,29.0,294.0,73.0:11,27.0,100.5,59.5:15,22.0,331.5,0.0:17,25.0,235.5,16.0:19,21.0,48.0,31.0:26,30.0,301.5,18.5:28,25.0,303.0,42.0
15888:NMEA:1362715917:$GPGSV,2,1,08,08,73,294,28,17,16,235,24,01,47,133,21,11,59,100,26*71
15889:NMEA:1362715917:$GPGSV,2,2,08,19,31,048,20,26,18,301,29,15,00,331,21,28,42,303,24*7D
15952:NMEA:1362715917:$GPGGA,041158.427,4738.283017,N,12207.949706,W,1,08,1.0,133.4,M,-17.2,M,,*67
15954:NMEA:1362715917:$GPRMC,041158.427,A,4738.283017,N,12207.949706,W,2.5,107.4,080313,,,A*7C
15957:GPSSC: 1st fix in:15938
gpsListener: received location (-122.132495,47.638050) accuracy: 5.000000
15964:GPSSC:STOPPED
---------- stopping ----------

## Slide 25: NMEA Sentences: $GPGSV
GPS Satellites in view
15888:NMEA:1362715917:$GPGSV,2,1,08,08,73,294,28,17,16,235,24,01,47,133,21,11,59,100,26*71
15889:NMEA:1362715917:$GPGSV,2,2,08,19,31,048,20,26,18,301,29,15,00,331,21,28,42,303,24*7D
1 = Total number of messages of this type in this cycle 2 = Message number 3 = Total number of SVs in view 4 = SV PRN number 5 = Elevation in degrees, 90 maximum 6 = Azimuth, degrees from true north, 000 to 359 7 = SNR, 00-99 dB (null when not tracking)
Repeat
Elevation angle
Azimuth angle

## Slide 26: NMEA Sentences : $GPGGA
Name | Example Data | Description
Sentence Identifier | $GPGGA | Global Positioning System Fix Data
Time | 041158.427 | 04:11:58.427
Latitude | 4738.283017,N | 47d 38. 283017' N
Longitude | 12207.949706,W | 122d 07.949706' W
Fix Quality: 0 = Invalid; 1 = GPS fix; 2 = DGPS fix | 1 | Data is from a GPS fix
Number of Satellites | 08 | 8 Satellites are in view
Horizontal Dilution of Precision (HDOP) | 1.0 | Relative accuracy of horizontal position
Altitude | 133.4, M | 133.4 meters above mean sea level
Height of geoid above WGS84 ellipsoid | -17.2, M | -17.2 meters
Time since last DGPS update | blank | No last update
DGPS reference station id | blank | No station id
Checksum | *75 | Used by program to check for transmission errors
15952:NMEA:1362715917:$GPGGA,041158.427,4738.283017,N,12207.949706,W,1,08,1.0,133.4,M,-17.2,M,,*67

## Slide 27: Summary
Acquisition
SV IDs
Baseband
Code Phases
Doppler
Tracking
Every ms continuous
1 ms data (4kB)
Intense computation
Decoding
Ephemeris
Time stamp
Time stamp: 6s
Ephemeris: 30s
TLM
HOW
Clock corrections and SV health
TLM
HOW
Ephemeris parameters
TLM
HOW
Almanac
TLM
HOW
Almanac, ionospheric model, dUTC
TLM
HOW
Ephemeris parameters
6
12
18
24
30
Time (sec)
300 bits (10 words)
preamble
Time of week
Code Phases
Least Square
(lat, lon)
~10ms
AP

## Slide 28: GPS Power Consumption (Succeeded)
Position Calculation
Acquisition
Tracking

## Slide 29: GPS Power Consumption (Failed)
Acquisition