## Slide 1
Solution
Green99: Saving Desktop Energy using SleepServer
Results
2. SleepServer takes over MAC/IP addr of sleeping machine by sending ARP Probe
Enable idle desktops to sleep, while minimizing disruption to users
Problem
3. Traffic meant for sleeping machine is redirected to sleep server
4. SleepServer wakes up sleeping machine by sending WoL upon receiving “important” traffic or events
5. Subsequent traffic is sent to the now-awake machine
WAN
Sleep Server
Sleeping Desktop
ARP
Probe
1. Idle machine informs SleepServer before going to sleep
WAN
Sleep Server
Idle Desktop
Subnet
Router
Subnet
Router
WAN
Sleep Server
Subnet
Router
Sleeping Desktop
WAN
Sleep Server
Subnet
Router
Desktop
Advantages
Your desktop is “always available”
Lightweight, easy to deploy
“Last man standing” configuration eliminates need for a dedicated sleep server
Seamless support for most corporate applications/protocols: RDP, SMB, RPC
SleepServer can do complex, stateful packet parsing
WoL
WAN
Sleep Server
Subnet
Router
Desktop
Live deployment in MSR
Used by 50+ users over 4 months
(Including lab director)
Typical machine sleeps > 40% of time
IT causes most wakeups
Sleeping machine responds in 8-9 seconds
Most of the savings come from long sleeps (typically at night)
Challenges
Joshua Reich (Intern), Michel Goraczko, Aman Kansal, Jitu Padhye – MSR Redmond
Existing connections break
Not a problem in typical
corporate environments.
Applications that depend on outgoing connections may be delayed (e.g. LiveMesh, LiveSync)
Notification