## Slide 1: Adapting Channel Widths to Improve Application Performance
Ranveer Chandra
Microsoft Research
Collaborators:
Victor Bahl, Ratul Mahajan, Thomas Moscibroda, Srihari Narlanka, Ramya Raghavendra

## Slide 2: Cognitive (Smart) Radios
Dynamically identify currently unused portions of spectrum
Configure radio to operate in available spectrum band
   take smart decisions how to share the spectrum
Signal Strength
Frequency
Frequency
Signal Strength

## Slide 3: Revisiting Channelization in 802.11
802.11 uses channels of fixed width
  20 MHz wide separated by 5 MHz each
Can we adapt channel widths?
When to change channel widths?
6
1
11
20 MHz
2402 MHz
2427 MHz
2452 MHz
2472 MHz
2
2407 MHz
3
2412 MHz

## Slide 4: Changing Channel Widths
Scheme 1: Turn off certain subcarriers ~ OFDMA
20 MHz
10 MHz
Issues: Guard band? Pilot tones? Modulation scheme?

## Slide 5: Changing Channel Widths
Scheme 2: reduce subcarrier spacing and width!
 Increase symbol interval
20 MHz
10 MHz
Properties: same # of subcarriers, same modulation

## Slide 6: Implementing Variable Channel Widths
Modify frequency of clock that drives PLL
  Implemented on Atheros cards – programmable clock
  Can generate 5, 10, 20, 40 MHz widths
MAC & PHY timing parameters scales with clock rate
  Symbol time: 4 s (20 MHz), 8 s (10 MHz)
  Guard Interval: 0.8 s (20 MHz), 1.6 s (10 MHz)
  We keep 802.11 slot time constant for interoperability

## Slide 7: Impact of Channel Width on Throughput
Throughput increases with channel width
  Theoretically, using Shannon’s equation
    Capacity = Bandwidth * log (1 + SNR)
  In practice, protocol overheads come into play
    Twice bandwidth has less than double throughput
Chart: Modulation
| 6 | 9 | 12 | 18 | 24 | 36 | 48 | 54
5 MHz | 1.26 | 1.87 | 2.41 | 3.37 | 4.27 | 5.77 | 6.86 | 7.42
10 MHz | 2.49 | 3.53 | 4.53 | 6.22 | 7.68 | 9.92 | 11.8 | 12.6
20 MHz | 4.73 | 6.55 | 8.04 | 10.7 | 12.8 | 15.8 | 18.4 | 19.3
40 MHz | 8.45 | 11.1 | 13.7 | 17.3 | 20.1 | 23.5 | 25.6 | 26.6

## Slide 8: Impact of Channel Width on Range
Chart: Attenuation (dB)
| 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85
5MHz | 0 | 0 | 0 | 0 | 0.033 | 0.049 | 0.106 | 0.35 | 1.325 | 3.7 | 4.12 | 5.24 | 6.24 | 6.5 | 6.234 | 7.25 | 8.35 | 16.47 | 100 | 100 | 100
10MHz | 0 | 0.032667 | 0 | 0.049 | 0.033 | 0.016 | 1.87 | 2.06 | 2.1 | 3.4 | 3.32 | 3.42 | 4.32 | 5.14 | 5.62 | 6.7 | 36.4 | 100 | 100 | 100 | 100
20MHz | 0.098 | 0.098667 | 0.065 | 0.033 | 0.049 | 0.56 | 1.26 | 1.36 | 1.63 | 2.5 | 3.67 | 4.134 | 10.45 | 23.62 | 34.26 | 100 | 100 | 100 | 100 | 100 | 100
40MHz | 2.8 | 3.6 | 3.8 | 4.6 | 4.62 | 5.23 | 5.38 | 5.6 | 7.36 | 10.6 | 13.64 | 18.45 | 43.9 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Reducing channel width increases range
  Narrow channel widths have same signal energy but lesser noise  better SNR
~ 3 dB

## Slide 9: Impact of Guard Interval
Reducing width increases guard interval  more resilience to delay spread (more range)
Chart: Delay Spread (in ns)
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
5MHz | 0 | 0 | 0 | 0.85 | 0.56 | 1.15 | 2.5 | 3.78 | 11.9 | 45.86 | 80.5 | 85 | 87.9 | 86 | 84.3 | 87.8 | 95.43 | 96.4 | 95.6 | 100 | 100
10MHz | 0 | 0 | 0.04 | 0.68 | 0.95 | 1.43 | 5.43 | 19.5 | 57.89 | 82.4 | 86.9 | 92.3 | 85.67 | 83.9 | 91.4 | 93.2 | 95.4 | 97.6 | 100 | 100 | 100
20MHz | 0 | 0.37 | 0.54 | 5.7 | 8.5 | 13.45 | 38.5 | 65.9 | 78.48 | 84.6 | 82.4 | 86.9 | 92.45 | 96.32 | 95 | 94.8 | 97.5 | 100 | 100 | 100 | 100
40MHz | 0 | 0 | 0.85 | 9.87 | 28.9 | 56.7 | 82.89 | 84 | 83.9 | 87 | 95.09 | 92.3 | 98 | 95 | 93.5 | 97 | 100 | 100 | 100 | 100 | 100

## Slide 10: Impact of Channel Width on Battery Drain
Lower channel widths consume less power
  Lower bandwidths run at lower processor clock speeds  lower battery power consumption
Lower widths increase range while consuming less power!

## Slide 11: Application 1: Song Sharing
Use narrowest width when searching for peers
(max range, least battery usage)
Algorithm (SampleWidth)
Adapt to best power-per-byte width
Chart: Energy (Joule)
| 5MHz | 10MHz | 20MHz | 40MHz | SW
 | 70.0519 | 69.7951 | 75.2548 | 87.1846 | 66.2559
Chart: Seconds
| 20 | 30 | 40 | 50
5MHz | 1042.236 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1059.3386 | 1383.2599 | 1378.0043 | 1382.2186 | 1381.1134 | 1375.9708 | 1381.6355 | 1382.2202 | 1383.7238 | 1380.6566 | 1381.6339 | 1379.0947 | 1376.9585 | 1380.136 | 1381.637 | 1382.7392 | 1374.3495 | 1385.8794 | 1380.5913 | 1381.6979 | 1380.6149 | 1378.5765 | 1371.2332 | 1054.2109 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1042.6875
10MHz | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1116.785 | 1386.1945 | 1385.4047 | 1382.0609 | 1382.1976 | 1385.1742 | 1381.8227 | 1386.1945 | 1385.6596 | 1381.3435 | 1382.5917 | 1384.4073 | 1386.6812 | 1354.7905 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924
20MHz | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1248.3184 | 1430.8855 | 1430.3708 | 1434.9943 | 1425.4995 | 1429.1425 | 1431.1212 | 1428.8872 | 1431.2454 | 1339.5631 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887
40MHz | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.5797 | 1567.6356 | 1566.5959 | 1568.0928 | 1565.6246 | 1567.175 | 1570.6025 | 1480.0706 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705
SW | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1297.058 | 1287.256 | 1345.3487 | 1472.979 | 1570.4584 | 1567.3442 | 1569.248 | 1591.3778 | 1439.1555 | 989.482 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115 | 1041.56 | 1042.0115

## Slide 12: Application 2: Increased Capacity
Contending flows on separate channels increases capacity
  Lesser contention overhead, no rate anomaly
Chart: Throughput (Mbps)
| Near-Near | Medium-near | Far-near
1x 40 MHz channel | 33.26 | 21.2527 | 14.305
2x 20 MHz channels | 36.44 | 25.9575 | 22.89

## Slide 13: Summary
Channel width is a powerful knob
  For better spectrum efficiency
  To improve application performance
  To design better, more efficient networks
Limitations/Future Work
  Nodes cannot communicate across channel widths
  Interference caused by narrow widths
  Systems that use adaptive channel widths (mesh networks, WLANs, …)