## Slide 1: Smartphones as distributed system with extreme heterogeneity
Lin Zhong
Rice Efficient Computing Group (recg.org)
Dept. of Electrical & Computer Engineering
Rice University

## Slide 2: Today’s smartphone
Application processor

## Slide 3
rackspace

## Slide 4: Heterogeneous multiprocessor
Application processor
µ-controller
Turducken-like systems

## Slide 5: Heterogeneous body-area network

## Slide 6: Smartphone 2020
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor

## Slide 7: Challenges to programming
Resource disparity
  ISA disparity
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor

## Slide 8: Challenges to programming
Resource limitation on “small” processors
  Virtual machine and coherent memory difficult
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor

## Slide 9: Challenges to programming
Separation of hardware vendors, application developers, and users
  Developer blind of external computing resources and runtime context
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor

## Slide 10: Challenges to programming
Established programming model and OS
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor

## Slide 11: Existing solutions
Complete transparency
No transparency
Single ISA
Prohibitively expensive
High burden on application developers
Virtual machine
Turducken-like cohort systems
Offloading systems (active disk, Hydra etc.)
CPU+GPU systems
mPlatform etc.

## Slide 12
Reflex: Transparent programming of heterogeneous mobile systems
http://reflex.recg.rice.edu/
Inspired by the heterogeneous distributed nervous system
Notes: http://scienceblogs.com/neurophilosophy/upload/2007/07/descartes-reflex.jpg

## Slide 13: Enough transparency
Reflex
Single ISA
Turducken-like cohort systems
Offloading systems (active disk, Hydra etc.)
Virtual machine
CPU+GPU systems
Complete transparency
No transparency
Ease of programming
Execution efficiency
mPlatform etc.

## Slide 14: Key ideas
Light weight virtualization of sensor data acquisition, timer, and memory management
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor

## Slide 15: Key ideas
Distributed runtime for transparent message passing
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Reflex runtime
Reflex runtime
Reflex runtime
Reflex runtime
Reflex runtime

## Slide 16: Key ideas
Automatic code partition through a collaboration between runtime and compiler
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Reflex runtime
Reflex runtime
Reflex runtime
Reflex runtime
Reflex runtime

## Slide 17: Key ideas
Identify a small coherent memory segment
  Maintain by message passing through the runtime
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Reflex runtime
Reflex runtime
Reflex runtime
Reflex runtime
Reflex runtime

## Slide 18: Key ideas
Type safety for dynamic process migration
Application processor
µ-controller
µ-controller
µ-controller
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Cloud processor
Reflex runtime
Reflex runtime
Reflex runtime
Reflex runtime
Reflex runtime

## Slide 19: Reflex Prototype (board integration)
Programmable accelerometer (TI MSP430)
Wired sensor through UART port
Rice Orbit Sensor
Nokia N810
Serial connection

## Slide 20: Fall detection with N810
Average Power
100mW
20mW
Legacy
Reflex
The secret: we do not fall very often

## Slide 21: Coded as part of Smartphone program
class SenseletFall : public SenseletBase {
public:
SenseletFall () { _avg_energy = 0; };
void OnCreate() { RegisterSensorData(ACCEL, 50); };
void OnData(uint8_t *readings, uint16_t len) {
uint16_t energy = readings[0]*readings[0] + \
readings[1]*readings[1] + \
readings[2]*readings[2];
//do a simple low-pass filtering
_avg_energy = _avg_energy / 2 + energy / 2;
// detect fall accident with the filtered energy
if (_avg_energy > THRESHOLD) {
theMainBody.FallAlert(); //RMI
}
}
void OnDestroy() { UnRegisterSensorData(ACCEL); };
private:
uint16_t _avg_energy;
};

## Slide 23: Even accelerometer is power-hungry!
2mW
90mW
7mW
Nokia N900
200mW
Standby
Accelerometer
Read
Read & simple calculation

## Slide 24: Energy-proportional computing
Energy consumption = a × Work
Work per unit time, e.g. CPU utilization and bandwidth utilization
Chart: 
| 0 | 1 | 20 | 40 | 80 | 100
Ideal: Power | 0 | 0.05 | 1 | 2 | 4 | 5

## Slide 25: Cruel reality: disproportionality
Energy = f (Work) + C
Work per unit time, e.g. CPU utilization and bandwidth utilization
Chart: 
| 0 | 1 | 20 | 40 | 80 | 100
Ideal: Power | 0 | 0.05 | 1 | 2 | 4 | 5
Power | 1 | 1.2439 | 4.1606 | 5.3233 | 5.9084 | 5.9663
Notes:   C: static power and system overhead
  Peak efficiency is usually achieved at peak performance (observed for both processors and wireless interfaces)

## Slide 26: Cruel reality: disproportionality
Energy = f (Work) + C
Work per unit time, e.g. CPU utilization and bandwidth utilization
Chart: 
| 0 | 1 | 20 | 40 | 80 | 100
Ideal: Power | 0 | 0.05 | 1 | 2 | 4 | 5
Ideal: Energy per work | 3 | 3 | 3 | 3 | 3 | 3
Power | 1 | 1.2439 | 4.1606 | 5.3233 | 5.9084 | 5.9663
Energy per work | 10000000 | 74.6312 | 12.4818 | 7.985 | 4.4313 | 3.5798
Notes:   C: static power and system overhead
  Peak efficiency is usually achieved at peak performance (observed for both processors and wireless interfaces)

## Slide 27: Ongoing work
Automatic code partition
Global variables/memory to a small coherent shared memory
Message passing to maintain the coherency