## Slide 1: 2018 Microsoft Indoor Localization Competition
Dimitrios Lymberopoulos (Microsoft Research)
Jie Liu (Microsoft Research)
Vitor Sequeira (European Commission – Joint Research Center)
Vivek Jain (Bosch)
Niki Trigoni (University of Oxford)
Anthony Rowe (CMU)
Nader Moayeri (NIST)
Organizers

## Slide 2: Competition Goals
Evaluate and compare technologies from academia and industry in the same, unfamiliar space.
Bring teams working in this area together in a more effective way.
2014: Berlin
2015: Seattle
2016: Vienna
2017: Pittsburgh

## Slide 3: 2018: Porto
34 teams submitted abstracts
26 systems officially registered
25 systems showed up in Porto
22 systems were evaluated

## Slide 4: Two Categories
2D Category
  Report (X,Y) locations
  Do not require the deployment of any infrastructure (WiFi and/or IMU based)
3D Category
  Report (X,Y,Z) locations
  Require custom hardware deployment (UWB, Ultrasound etc.)
  Each team can deploy up to 10 anchor devices in the evaluation space

## Slide 5: Evaluation Process
Day 1: Tuesday
  Teams were given 8 hours to setup and calibrate their systems.
Day 2: Wednesday
  Each team mounted their systems on our evaluation backpack and continuously logged locations over a predetermined path.
Evaluation Metric
  Average localization error across all recorded points along the path.
  The lower the error the better.
LiDAR
System under Test

## Slide 6: Evaluation Area - Two Floors

## Slide 7: Ground Truth Measurements & Evaluation
The ground truth environment and the test points were acquired using multiple high definition 3D scans using a tripod mounted laser scanner (e.g. ZF 5006) and proprietary software
High Resolution 3D Acquisition and Registration
Pierluigi Taddei
Carlos Sanchez
JRC (https://ec.europa.eu/jrc), the winner of the 2015 competition, volunteered to provide its expertise for ground truth measurements.
JRC has been deploying 3D laser scanning technology to verify design information within nuclear facilities for more than 10 years.
Vitor Sequeira

## Slide 8: 2D Results
Chart: Team
| *Naviguy | Ariel Univ. (Step) | *Ali et al. | Ariel Univ. (GoIn) | Rea et al. | Naviguy (Fusion) | *Fineway
*Naviguy Ariel Univ. (Step) *Ali et al. Ariel Univ. (GoIn) Rea et al. Naviguy (Fusion) *Fineway | 2.3 | 2.4 | 3.2 | 4.3 | 5.3 | 9.4 | 12.5
PDR
PDR + Fingerprinting
WiFi ToF
Camera+PDR
Camera+PDR+Finger.
Teams that start with * require initialization.
Naviguy and Ariel Univ. were considered a tie! Ariel University is the winner as Naviguy required initialization while Ariel University did not.
Naviguy
Ariel Univ. (Step)

## Slide 9: 3D Results
Chart: 
| CMU | SND Smart Ltd | Yodel Labs | Zhejiang Univ. (AID) | Zhejiang Univ. (RA2) | RaceLogic | McMaster | TU Braunschweig | Aachen University | TU Dortmund | Aachen University (coop.) | *VL-Loc | Intellidom | National Research Univ. | Zhejiang Univ (AA)
 | 0.27 | 0.4 | 0.47 | 0.7 | 0.71 | 0.73 | 0.94 | 0.99 | 1.16 | 1.21 | 1.49 | 1.7 | 3.79 | 6.94 | 16.64
Sound
Atmel
Phase
Sound+ ARKit
UWB+
ARKit
UWB
Camera+
LED + PDR
Teams that start with * require initialization. SND Smart Ltd and Yodel Labs are considered a tie!

## Slide 10: 3D Results
Chart: 
| CMU | SND Smart Ltd | Yodel Labs | Zhejiang Univ. (AID) | Zhejiang Univ. (RA2) | RaceLogic | McMaster | TU Braunschweig | Aachen University | TU Dortmund | Aachen University (coop.) | *VL-Loc | Intellidom | National Research Univ. | Zhejiang Univ (AA)
 | 0.27 | 0.4 | 0.47 | 0.7 | 0.71 | 0.73 | 0.94 | 0.99 | 1.16 | 1.21 | 1.49 | 1.7 | 3.79 | 6.94 | 16.64
Sound
Atmel
Phase
Sound+ ARKit
UWB+
ARKit
UWB
Camera+
LED + PDR

## Slide 11: 3D Results
Chart: 
| CMU | SND Smart Ltd | Yodel Labs | Zhejiang Univ. (AID) | Zhejiang Univ. (RA2) | RaceLogic | McMaster | TU Braunschweig | Aachen University | TU Dortmund | Aachen University (coop.) | *VL-Loc | Intellidom | National Research Univ. | Zhejiang Univ (AA)
 | 0.27 | 0.4 | 0.47 | 0.7 | 0.71 | 0.73 | 0.94 | 0.99 | 1.16 | 1.21 | 1.49 | 1.7 | 3.79 | 6.94 | 16.64
Sound
Atmel
Phase
Sound+ ARKit
UWB+
ARKit
UWB
Camera+
LED + PDR

## Slide 12: 3D Results
Chart: 
| CMU | SND Smart Ltd | Yodel Labs | Zhejiang Univ. (AID) | Zhejiang Univ. (RA2) | RaceLogic | McMaster | TU Braunschweig | Aachen University | TU Dortmund | Aachen University (coop.) | *VL-Loc | Intellidom | National Research Univ. | Zhejiang Univ (AA)
 | 0.27 | 0.4 | 0.47 | 0.7 | 0.71 | 0.73 | 0.94 | 0.99 | 1.16 | 1.21 | 1.49 | 1.7 | 3.79 | 6.94 | 16.64
Sound
Atmel
Phase
Sound+ ARKit
UWB+
ARKit
UWB
Camera+
LED + PDR

## Slide 13: 3D Results
Chart: 
| CMU | SND Smart Ltd | Yodel Labs | Zhejiang Univ. (AID) | Zhejiang Univ. (RA2) | RaceLogic | McMaster | TU Braunschweig | Aachen University | TU Dortmund | Aachen University (coop.) | *VL-Loc | Intellidom | National Research Univ. | Zhejiang Univ (AA)
 | 0.27 | 0.4 | 0.47 | 0.7 | 0.71 | 0.73 | 0.94 | 0.99 | 1.16 | 1.21 | 1.49 | 1.7 | 3.79 | 6.94 | 16.64
Sound
Atmel
Phase
Sound+ ARKit
UWB+
ARKit
UWB
Camera+
LED + PDR

## Slide 14: 3D Results
Chart: 
| CMU | SND Smart Ltd | Yodel Labs | Zhejiang Univ. (AID) | Zhejiang Univ. (RA2) | RaceLogic | McMaster | TU Braunschweig | Aachen University | TU Dortmund | Aachen University (coop.) | *VL-Loc | Intellidom | National Research Univ. | Zhejiang Univ (AA)
 | 0.27 | 0.4 | 0.47 | 0.7 | 0.71 | 0.73 | 0.94 | 0.99 | 1.16 | 1.21 | 1.49 | 1.7 | 3.79 | 6.94 | 16.64
Sound
Atmel
Phase
Sound+ ARKit
UWB+
ARKit
UWB
Camera+
LED + PDR

## Slide 15
1st
2nd
2nd
2D Category
3D Category
$1000
$600
$600
Steps – An Accurate Relative Positioning Method for First-Responders
Landau et al.
(Ariel University)
2.4m error
Realty and Reality: Where Location Matters
Miller et al.
(CMU)
0.27m error
Inertial Sensing Approach for Indoor Localization
Qu et al.
(Naviguy/Tongji University)
2.3m error
NavInThings – An Indoor Localization and Navigation UWB System
Gao et al.
(SND Smart Ltd/ATE Electronics Ltd)
0.40m error
ALPS: The Acoustic Location Processing System
Lazik et al.
(Yodel Labs)
0.47m error